## Slide 1: NanoEdge AI Studio to STM32CubeIDE app that recieves Anomaly Detection input via COM Port
No Physical Sensors Required
Presenter Stephen MacKenzie

## Slide 2: Resources
Download NanoEdge AI Studio:
  https://stm32ai.st.com/download-nanoedgeai/
ST Electronics NanoEdge AI Studio docs and tutorials:
  https://wiki.st.com/stm32mcu/wiki/Category:NanoEdgeAI
Anomaly Detection YouTube from ST:
  https://www.youtube.com/watch?v=yXMUv_C5FGk
My GibHub (links to the project(s), see last slide)
  https://github.com/stevemac321

## Slide 3: Overview – The Goal
Build and demonstrate a functional anomaly detection pipeline with:
  No physical sensor input
  Simple pattern signal files, spaces and comma delim.
  An STM32 board with ST-Link over USB
  Core logic spanning NanoEdge AI Studio → Embedded App → COM port client

## Slide 4: GitHub Project Structure
anomaly_spaces_for_nanoedge.csv,regular_spaces_for_nanoedge.csv for NanoEdge AI Studio signal input.
  Anomaly.csv 5x140, regular.csv 20x140 for client-controller runtime.
Embedded STM32CubeIDE project
  USB STLink on COM Port
  USART enabled, interrupt enabled
NanoEdge AI Studio benchmarked algorithm, lib and header
  Already “deployed” into Core/Inc and Core/lib into the STMCubeIDE project
Python clients, console and option QT PySide6.

## Slide 5: Recommended WorkFlow for Portability
Clone the NanoEdge_Anomaly_Detection project from:
  https://github.com/stevemac321/NanoEdgeAI_Anomaly_Detection
  This gives you access to main.c and stm32xxxx_it interrupt code
  Signal files, you skip the NanoEdge AI Studio if you want and just get the header and lib from Core/Inc and Core/Lib
Create New STM32CubeIDE project for your board (unless you have a NUCLEO-H723ZG)
  Enable USART (I use usart3 or whatever shares STLK_VCP_RX/TX)
  Make sure baud rate matches your STLink COM port Enable interrupts,on windows open Device Manager (see readme for Linux)

## Slide 6: NanoEdge AI Studio — Creating the Anomaly Detection Model
New Project →Anomaly Detection
Import signals
  regular_spaces_for_nanoedge.csv
  anomaly_spaces_for_nanoedge.csv
Run Benchmark to evaluate candidate models
Validation tab to choose best lib
Deploy, creates emulator, lib, and header(s)

## Slide 7: Deploying the zipfile to the STMCube32IDE app
Create STM32CubeIDE app for your board
STM32CubeIDE app
Extract zip
  Copy NanoEdgeAI.h to STMCubeIDE Project: Core/Inc
  Copy libneai.a to Core/lib
Add libpath to Core/lib in project properties:
  C/C++ General →Library Paths (add /<projectdirectory>/Core/lib)
  C/C++ General →Libraries (add neai, not libneai and no file extension .a)

## Slide 8: Adding Training and Detection Code to the STM32CubeIDE embedded app
You can just copy the cloned main.c into your project or these steps:
In USER CODE BEGIN Includes section of main.c
  Include headers: NanoEdgeAI.h, string.h (for memcpy), optional stdio.h for printf (you will need a _write function, its in the cloned main.c.
In USER CODE BEGIN PM, #define DATA_INPUT_USER 140
In USER CODE BEGIN PV:
  static float EKG_Input[DATA_INPUT_USER];// pass to model
  static uint8_t rx_chunk[4]; // Temporary buffer to hold 4 bytes of one float
  static uint16_t ekg_index = 0; // Index into EKG_Input
  extern float training_data[][DATA_INPUT_USER];
  extern size_t training_data_len;

## Slide 9: Adding Code in main.c (continued)
In USER CODE BEGIN PFP add:
  enum neai_state train_model();
In USER CODE BEGIN WHILE add: (see cloned main.c)
  if (train_model() != NEAI_MINIMAL_RECOMMENDED_LEARNING_DONE) {
  HAL_UART_Abort_IT(&huart3);
  __HAL_UART_DISABLE_IT(&huart3, UART_IT_RXNE);
  } else {
  // Start UART receive in interrupt mode
  // Request the next 4 bytes (one float)
  HAL_StatusTypeDef hal_ret = HAL_UART_Receive_IT(&huart3, rx_chunk, sizeof(rx_chunk));
    if(hal_ret != HAL_OK) {
    //printf("receiveIT failed %d", hal_ret);
    return 0;
  }
  }

## Slide 10: Adding Code in main.c (more continued)
In USER CODE BEGIN PFP add:
  enum neai_state train_model();
In USER CODE BEGIN WHILE add: the code cloned main.c that calls train_model
In USER CODE BEGIN 4 (or whatever), add implementations:
  _write (optional if you want printf
  RxCpltCallback
  train_model

## Slide 11: Adding Interrupt Code
Open the cloned Core/Src/stm32h7xx_it.c file, find:
  USART3_IRQHandler
    Make sure that HAL_UART_IRQHandler is called in your generated stm32xxxx_it.c file.
  Add this the code in USER CODE BEGIN USART3_IRQn 1:
    HAL_UART_RxCpltCallback into your stm32xxxx_it.c file.

## Slide 12: Build, Debug
Build the STM32CubeIDE project
Debug (will flash your board)
Once it is flashed, it will run, debugging is optional
To send the board data, on your host run: “python EKG_Simulator.py
If you want to debug, set a breakpoint in HAL_UART_RxCpltCallback, inspect:
  Status (see NanoEdgeAI.h for enum values)
  Simularity (100 is “most regular”, 0 is “most anomaly”
  EKG_Input is the float array buffer from uint8_t rx_chunk from HAL_UART_Receive_IT, check rx_chunk too.

## Slide 13: EKG_Simulator Results
Return bytes
Neai status
Simularity (100 normal, 0 anomaly)
There are just two samples hardcoded
There is another project you can clone for a bit more variety:
  https://github.com/stevemac321/NanoEdge_Client
  This is a QT PySide6 app (see the readme in that project)

## Slide 14: Links
This project enlistment:
  https://github.com/stevemac321/NanoEdgeAI_Anomaly_Detection
QT PySide6 Client enlistment:
  https://github.com/stevemac321/NanoEdge_Client
About Me:
  https://www.linkedin.com/in/stevemac321/
My Music and Technology YouTube Channel:
  https://www.youtube.com/@stephenmackenzie6782